## Slide 1
Developing a Highly Parallelized TCR Synthesis Algorithm on GPGU and FPGA for Acceleration the Study of Immune System
Elnaz Tavakoli Yazdi
Advisor: Ali Akoglu
Committee: Salim Hariri and Tosiron Adegbija
University of Arizona
Department of Electrical and Computer Engineering
tavakoliyazdi@email.arizona.edu

## Slide 2: Outline
V(D)J recombination process
  Biological perspective
  Algorithmic perspective
GPU implementations
  Baseline GPU implementation
  Bit-wise GPU implementation
  Multi-GPU implementation
FPGA implementations
  N-level parallelization method
  VJ-level parallelization method
Summary
Future work

## Slide 3: V(D)J Recombination Process

## Slide 4: Motivation- DNA Recombination
Immune systems of jawed vertebrates depend on DNA (VDJ) recombination
  determines diversity of antigen receptors; Immunoglobulins, T-cell receptors (TCRs)
Modelling TCR repertoire
  helps scientists to understand immune system responses to foreign antigens
  enables immunologists to test the validity of their assumptions and solve their fundamental question
Peta-scale Computing
  Mouse data set contains sequences and potential paths
  For human data set, the scale of the data increases to and potential paths

## Slide 5: V(D)J Recombination Algorithm
Consists of the rearrangement of sets of:
  Variable (V) Genes (20 sequences)
    362 possible termini variations
  Diversity (D) Genes (2 sequences)
    230 paths for DB1
    275 paths for DB2
  Joining (J) Genes (12 sequences)
    283 possible variations
Each sequence is generated using four bases (A, C, T, G)
Non-templated (n) -Nucleotides create additional diversity at VDJ junctions
  4m (m is length of ‘N’)

## Slide 6: V(D)J Recombination Algorithm
Consists of three steps:
  Step Zero
  Step One

## Slide 7: V(D)J Recombination Algorithm
  Step Two
  Step Three

## Slide 8: V(D)J Recombination Algorithm
Recombination process from algorithmic respective

## Slide 9: True V(D)J problem size
Possible Recombination Paths with m=10: 398,292,334,673,920

## Slide 10: GPU Implementations

## Slide 11: Baseline GPU Implementation
An n-level parallelization approach
  Each thread generates a unique n-nucleotide
  Total threads launched is based on length of nucleotide: 4m threads (always divisible by warp-size when m > 2)
  Each thread performs its own recombination with V, D, and J
with global memory coalescing, shared memory broadcasting, and very fine granularity
  G. Striemer, H. Krovi, A. Akoglu, B. Vincent, B. Hopson, J. Frelinger, and A. Buntzman, “Overcoming the limitations posed by tcrβ repertoire modeling through a gpu-based in-silico dna recombination algorithm," in IEEE Proceeding 28th Int. Parallel and Distributed Processing Symp, pp. 231-240, May 2014.

## Slide 12: Contributions
Devising a bit-wise GPU-based implementation of recombination process
Extending the bit-wise implementation to a multi-GPU environment
Utilizing the N-level parallelization approach for the FPGA-based implementation of the recombination process
Devising a VJ-level parallelization approach for FPGA implementation

## Slide 13: Bit-wise GPU Implementation
Representing each base with two bits
  Reducing memory footprint
  Fetching four characters with one memory access
Zero padding sequences to be divisible by eight
  Padded bits
  Full byte

## Slide 14: Bit-wise GPU Implementation
N-Level parallelization approach
  Task generator
In vivo sequences are partitioned into 240 groups
  20 V gene
  12 J gene

## Slide 15: Bit-wise GPU Implementation
Comparison process

## Slide 16: Experimental Results for GPU Implementation
Thread-block Configuration analysis
  Normalized value of 1 represents the
  best performance for a given length
  20% reduction in performance of n=7
  for 256 threads per block
    Lower thread-block utilization
  35% reduction in performance
  of n= 8 for 32 threads per block
Thread-block configuration
  64 for n length 4 to 8
  128 for n length 9 and 10

## Slide 17: Bit-wise Simulation Results
Memory Footprint
  Reducing constant memory by
  a factor of 3.4
  Reducing global memory by
  a factor of 4

## Slide 18: Bit-wise Simulation Results
Execution Time
  Reducing total execution time by
  a factor of 2.1

## Slide 19: Multi-GPU Implementation
Defining global Index
Workload distribution
Performing reduction process
  Collecting results to the root node

## Slide 20: Multi-GPU Simulation Results
Execution Time
  Slight increase for n-nucleotide length of less than eight
  Observing the benefit from a multi-GPU environment for n-nucleotide length of greater than seven
  Increase in execution time by about a factor of four at each increments of the n-nucleotide length
  Almost same execution time for two consecutive n lengths, while using one GPU and four GPUs

## Slide 21: Multi-GPU Simulation Results
Execution Time

## Slide 22: FPGA Implementations

## Slide 23: Architecture I
Hardware architecture for N-level parallelization approach

## Slide 24: Architecture I
Hardware architecture for N-level parallelization approach

## Slide 25: Simulation Results for N-Level Parallelization
Resource Utilization

## Slide 26: Simulation Results for N-Level Parallelization
Execution Time

## Slide 27: Advantages and Disadvantages of N-level method
Advantages
  Even workload distribution across CUs
  Parallel comparison process
  Elimination of the repetitive computations for generating in silico sequences.
Disadvantages
  Large critical path delay
    due to the communication between the n-sequence initiator unit and CUs
  No overlap between the execution of two consecutive component

## Slide 28: Architecture II
Hardware architecture for VJ-level parallelization approach

## Slide 29: Architecture II
Hardware architecture for VJ-level parallelization approach

## Slide 30: Simulation Results for VJ-Level Architecture
Resource Utilization

## Slide 31: Simulation Results for VJ-Level Architecture
Execution Time

## Slide 32: Summary and Future Work

## Slide 33: Summary
Devising a bit-wise GPU-based implementation of the V (D)J recombination algorithm
  Reduces the constant memory and global memory footprint by factors of 3.4 and 4
  Reducing the execution time by a factor of 2.1
Presenting a multi-GPU implementation for the bitwise recombination
  Reduces the execution time with increasing the number of GPUs
Mapping the recombination process on FPGA using N-level method
Developing a VJ-level parallelization method for the FPGA implementation
  Reducing the execution time by a factor of 2.3 in comparison with N-level method

## Slide 34: Future Work
Expand to research recombination repertoire of humans
  Currently have 50 million sequences from 100 humans
  Several formats require significant pre-processing
Additional performance optimizations
  Proposing scalable implementation of recombination process for the multi-GPU environment
  Utilizing hash function to speed up the comparison process

## Slide 35: Questions?

## Slide 36
Additional Slides

## Slide 37: V(D)J Recombination Algorithm

## Slide 38: Baseline GPU-based Implementation

## Slide 39: Baseline GPU-based Implementation

## Slide 40: FPGA-based Implementation
Determining the degree of parallelism
  Correlation between Dp and resource utilization.
  Resource utilization for a single computation unit (CU)
  Correlation between Dp and critical path delay

## Slide 41: FPGA-based Implementation
Hardware architecture for N-level parallelization approach
  Address Generator Unit (AGU)
    Generating address for V, D, and J memory bank units
  Memory bank Unit
    J Memory
      Containing all 12 J sequence with the chewback and palindromic forms
    V Memory
      Containing all 20 V sequence with the chewback and palindromic forms
    D Memory
      Containing D1 and D2 sequence with the chewback and palindromic forms
    In-vivo Memory
      Containing 240 BRAMs which keep one VJ group of in vivo sequence
    Counter Memory
      Containing 240 BRAMs which are assigned to one VJ group

## Slide 42: FPGA-based Implementation
  Processing Unit (PU)
    N-nucleotide Initiator Unit
      sending Initial n-nucletotide as a reference starting address to all CUs

## Slide 43: FPGA-based Implementation
  Processing Element(PU)
  Computation Unit
    Concatenation Unit
      using an or gate to concatenate the V , n1, D, n2 and J sequences in the given order to form a 128-bit sequence
    Comparison Unit
      Using 128-bit comparator
  In vivo Address Generator Unit
    Generating address for In-vivo and counter memory bank units
    Containing two arrays (startingarray, endingarray )
      Size of 19*240
      Determining the address based on the VJ group and length of in silico sequence

## Slide 44: FPGA-based Implementation
Hardware architecture for VJ-level parallelization approach
  Memory bank Unit
    J Memory
      Containing two J sequences with the chewback and palindromic forms
    V Memory
      Containing one V sequence with the chewback and palindromic forms
    D Memory
      Containing D1 and D2 sequence with the chewback and palindromic forms
    In-vivo Memory
      Containing two BRAMs in which each keeps one VJ group of in vivo sequence
    Counter Memory
      Containing two BRAMs in which each is assigned to one VJ group of in vivo

## Slide 45: FPGA-based Implementation
Hardware architecture for VJ-level parallelization approach
  Combination Unit
    Consists of five steps
      Calculating the length of in silico sequence and check its validity
      Setting the length of n1 and n2 sequence
      Calculating shift amount for each sequence and do concatenation
      Checking the status of FIFO and pass the in silico sequence if not full
      Adjusting the length of n1 and n2 nucleotide along with the binary value of n-nucleotide sequenc

## Slide 46: FPGA-based Implementation
Hardware architecture for VJ-level parallelization approach
  Comparison Unit
    Consists of five steps
      Checking the status of FIFO to have at least four sequences
      Reading one or four in silico sequence from buffer
      Extracting the length and groupid of in silico sequence
      Comparing the in vivo sequence with fetched sequences
      Updating counter memory

## Slide 47: FPGA-based Implementation
Hardware architecture for VJ-level parallelization approach
  FIFO
    Eliminate the communication between units
    Overlapping between the execution of two consecutive units
    Performing parallel comparison
  Determining size of FIFO
    Remaining below 85% BRAM utilization
    Assigning 1 × 36Kb BRAM to each PU
    Up to 256 in silico sequences

## Slide 48: FPGA-based Implementation