## Slide 1: Bit-wise and Multi-GPU Implementations of the DNA Recombination Algorithm
Elnaz Tavakoli Yazdi, Ankur Limaye, Ali Akoglu, Tosiron Adegbija, and Adam Buntzman
Department of Electrical and Computer Engineering, The University of Arizona, Tucson, AZ 85721

## Slide 2: Outline
Motivation
V(D) J Recombination Process
  Biological Perspective
  Algorithmic Perspective
GPU implementations
  Baseline GPU implementation
  Bit-wise GPU implementation
  Multi-GPU implementation
Results
Future work

## Slide 3: Motivation
DNA recombination essential for immune systems of jawed vertebrates
  determines diversity of antigen receptors; Immunoglobulins, T-cell receptors (TCRs)
  TCR recognizes an antigen, which induces immune system response to eliminate the antigen
Modeling the TCR repertoire
  Helps researchers to understand the immune system responses to foreign antigens
  Enables immunologists to test the validity of their assumptions and solve their fundamental question
Peta-scale Computing
  Mouse data set contains 105 sequences and potential 1015 paths
  For human data set, the scale of the data increases to 107 and potential paths 1018
Simulating the recombination process is time consuming
  Striemer et al. successfully modeled the mouse TCR repertoire for the first time
  Simulation time: 16 days (NVIDIA GTX480 GPU), estimated 52 weeks on a general-purpose processor
G. Striemer, H. Krovi, A. Akoglu, B. Vincent, B. Hopson, J. Frelinger, and A. Buntzman, “Overcoming the limitations posed by TCR repertoire modeling through a GPU-Based in-silico DNA recombination algorithm,” in Parallel and Distributed Processing Symposium, pp. 231–240, May 2014.

## Slide 4: V(D)J Recombination Algorithm
Immune systems achieve diversity in TCR repertoire through V(D)J recombination process
  Involves a rearrangement of the variable (V), diversity (D), and joining (J) gene segments in a combinatorial way chosen from members of each gene family
In mice, it consists of the rearrangement of sets of
  20 sequences of V genes with 362 possible termini variations
  2 sequences of D genes with 230 paths for DB1 and 275 paths for DB2 variations
  12 sequences of J genes with 283 possible termini variations
Each sequence is generated using four bases (A, C, T, G)
Non-templated (n) -Nucleotides create additional diversity at V(D)J junctions
  4m (m is length of ‘N’)
D. G. Schatz, and Y. Ji, “Recombination centers and the orchestration of V(D)J recombination,” Nature Reviews Immunology, vol. 11, No. 4, pp. 251–263, April 2011

## Slide 5: V(D)J Recombination Algorithm
Consists of three steps:
  Step Zero:
  a
  A
  A
  Step One:

## Slide 6: V(D)J Recombination Algorithm
  Step Two:
  a
  A
  aA
  Step Three:

## Slide 7: V(D)J Recombination Algorithm
Algorithmic perspective:

## Slide 8: V(D)J Recombination Algorithm Problem Size
Possible recombination paths for m=10 : 398,292,334,673,920

## Slide 9: Baseline GPU Implementation
An n-level parallelization approach
  Each thread generates a unique n-nucleotide
  Total threads launched is based on length of nucleotide: 4m threads (always divisible by warp-size when m > 2)
  Each thread performs its own recombination with V, D, and J
With global memory coalescing, shared memory broadcasting, and very fine granularity
  G. Striemer, H. Krovi, A. Akoglu, B. Vincent, B. Hopson, J. Frelinger, and A. Buntzman, “Overcoming the limitations posed by tcrβ repertoire modeling through a gpu-ased in-silico dna recombination algorithm," in IEEE Proceeding 28th Int. Parallel and Distributed Processing Symp, pp. 231-240, May 2014.

## Slide 10: Contributions
Devising a bit-wise GPU-based implementation of recombination process
Extending the bit-wise implementation to a multi-GPU environment
Utilizing the N-level parallelization approach for the recombination process

## Slide 11: Experimental Setup
P100 GPU Streaming Multiprocessor

## Slide 12: Bit-wise GPU Implementation
Representing each base with two bits
  Reducing memory footprint
  Fetching four characters with one memory access
Zero padding sequences to be divisible by eight
  Padded bits
  Full byte

## Slide 13: Bit-wise GPU Implementation
N-Level parallelization approach
  Task generator
In vivo sequences are partitioned into 240 groups
  20 V gene
  12 J gene

## Slide 14: Bit-wise GPU Implementation
Comparison Process:

## Slide 15: GPU Implementation Results
Thread-block Configuration analysis
  Normalized value of 1 represents the best performance for a given length
  20% reduction in performance of n=7 for 256 threads per block (tpb)
    Lower thread-block utilization
  35% reduction in performance of n= 8 for 32 tpb
Thread-block configuration
  64 for n length 4 to 8
  128 for n length 9 and 10

## Slide 16: Bit-wise Simulation Results
Memory Footprint
  Reducing constant memory by a factor of 3.4x
  Reducing global memory by a factor of 4

## Slide 17: Bit-wise Simulation Results
Execution Time
  Reducing total execution time by a factor of 2.1

## Slide 18: Multi-GPU Implementation
Defining the global Index:
Workload distribution
Performing reduction process
  Collecting results to the root node

## Slide 19: Multi-GPU Simulation Results
Execution Time
  Slight increase for n-nucleotide length of less than eight
  Observing the benefit from a multi-GPU environment for n-nucleotide length of greater than seven
  Increase in execution time by about a factor of four at each increments of the n-nucleotide length
  Almost same execution time for two consecutive n lengths, while using one GPU and four GPUs

## Slide 20: Multi-GPU Simulation Results
Execution Time

## Slide 21: Future Work
Expand to research recombination repertoire of humans
  Currently have 50 million sequences from 100 humans
  Several formats require significant pre-processing
Additional performance optimizations
  Proposing scalable implementation of recombination process for the multi-GPU environment
  Utilizing hash function to speed up the comparison process